Advanced DSP Workflow: From Raw Signal to Pattern Extraction and Statistical Analysis

Procedure:

Step1: Spectrogram visualization of real time data:

- Objective: The spectrogram is generated to analyze the time-varying frequency content of the original signal (eg:ocusync data).
- Visualization:
  - The x-axis represents time in seconds, illustrating the signal's evolution over time.
  - The y-axis shows the frequency spectrum in Hz, providing insight into the signal's frequency components.
  - The color scale indicates the signal's intensity (power) at each frequency and time point, with intensity levels shown in decibels (dB).
- Purpose: This method helps reveal how the signal's frequency content changes over time, making it useful for identifying frequency shifts, transient behavior, or patterns that occur at specific times in time-varying signals.

Step2: Sectral Analysis for data in frequency domain:
### Power Spectral Density (PSD) Calculation and Plotting:
After visualizing the spectrogram of the data we perform the following steps to calculate and plot the Power Spectral Density (PSD):
1. Windowing: A Hamming window is applied to the signal to minimize spectral leakage.
2. PSD Calculation: Welch's method is used to estimate the PSD by dividing the signal into overlapping segments, applying the FFT to each segment, and averaging the results.
3. Frequency Shifting: The frequency and PSD are shifted to account for both positive and negative frequencies.
4. Mean PSD: The mean PSD value is calculated and displayed.
5. Plotting: A logarithmic plot of the PSD is generated, with the mean PSD highlighted by a red dashed line.
This method provides a smooth estimate of the signal's power distribution across different frequencies, enabling a clearer analysis of the signal's frequency content.
- Analyzing the Frequency Spectrum of a Signal:
1. Perform the FFT: Compute the Fast Fourier Transform (FFT) of the Original signal (eg: ocusync data) to convert it from the time domain to the frequency domain.
2. Shift the Zero Frequency Component: Use a frequency shift to move the zero frequency component to the center of the frequency spectrum for easier visualization of both positive and negative frequencies.
3. Create the Frequency Axis: Generate the frequency axis corresponding to the FFT results using the sampling rate and the number of data points.
4. Plot the Magnitude of the FFT: Plot the magnitude of the frequency components to visualize the signal’s distribution across different frequencies, showing how much power is present at each frequency.
These steps help in understanding the frequency content of a signal, providing insights into its spectral characteristics.

Step3: Develop energy based algorithm to detect and extract n number of signal packets:
### General Working Procedure for Signal Packet Detection and Extraction :
1. Bandpass Filter Application:
  1. Objective: Isolate the desired frequency range by removing unwanted frequencies.
  2. Action: Apply a bandpass filter to the input signal using a specified frequency range (e.g., low and high cutoff frequencies).
    1. The filter is designed based on the Nyquist frequency, with cutoff frequencies normalized and applied using a filter function (e.g., butter and filtfilt).
  3. Outcome: The filtered signal contains only the frequency components within the specified range, eliminating out-of-band noise and other signals.
2. Energy Profile Calculation:
  1. Objective: Measure the signal's energy over time to identify regions with significant activity.
  2. Action: Compute the energy profile of the filtered signal by applying a sliding window approach.
    1. Energy is calculated as the squared magnitude of the signal, and a moving average or convolution is applied to this squared signal.
  3. Outcome: The energy profile provides a time-series representation of the signal's energy, highlighting periods of high activity or potential signal packets.
3. Threshold Calculation:
  1. Objective: Establish an energy threshold above which the signal is considered to contain valid packets.
  2. Action: Calculate the energy threshold by scaling the mean energy of the signal (usually representing noise) by a specified threshold factor.
  3. Outcome: The threshold helps distinguish signal packets (high energy) from background noise (low energy).
4. Packet Detection:
  1. Objective: Identify the start and end points of signal packets based on the energy profile and threshold.
  2. Action: Compare the energy profile to the threshold:
    1. If energy exceeds the threshold, mark the start of a packet.
    2. If energy falls below the threshold, mark the end of the packet.
  3. Outcome: A list of detected packets is created, where each packet is represented by its start and end indices in the signal.
5. Energy Profile Visualization:
  1. Objective: Visualize the energy profile and threshold to confirm packet detection.
  2. Action: Generate a plot showing the energy profile over time, with the threshold clearly marked.
    1. The energy profile is plotted as a continuous line, and the threshold is shown as a reference line (e.g., dashed).
  3. Outcome: The plot visually highlights the regions where energy exceeds the threshold, indicating detected packets.
6. Extract and Plot Detected Packets:
  1. Objective: Extract the identified signal packets and analyze them visually.
  2. Action: For each detected packet, calculate the start and end times based on sample indices.
    1. Extract the corresponding signal data and generate plots for each packet's amplitude over time.
  3. Outcome: The start time, end time, and duration of each packet are printed, and plots of the extracted packets are displayed for further analysis.
This general procedure isolates and extracts signal packets by filtering the signal, calculating energy profiles, detecting packets based on energy thresholds, and visualizing the results to ensure accurate packet detection.
Step4: Spectrogram visualization of all extracted packets:
Generate spectrograms for all extracted packets to analyze frequency content.
Step5: Estimate frequency offset for all signal packets:
1. Objective:
   Frequency offset estimation is needed to correct the frequency shift in received signal packets, which can occur due to factors like Doppler shift, hardware inaccuracies, or transmission conditions. Correcting this offset helps in accurate signal demodulation and further processing.
2. Method Applied:
  1. The Power Spectral Density (PSD) of the signal is calculated using the Welch method, which provides a frequency-domain representation of the signal's power.
  2. A Hamming window is applied to reduce spectral leakage.
  3. The consecutive method groups contiguous regions in the PSD that exceed a threshold, indicating potential frequency bands.
  4. The frequency offset is estimated by analyzing the identified frequency bands and checking if they fall within predefined offset ranges
  5. If a valid band is found, the frequency offset is determined based on the start and end frequencies of that band.
3. Outcome:
   The estimated frequency offset helps in compensating for shifts, allowing for more accurate signal analysis and processing.

Step6: Frequency offset correction for all signal packets:
### Method for Correcting Frequency Offset:
1. Offset Estimation:
  1. First, the frequency offset of each signal packet is estimated using Power Spectral Density (PSD) analysis. The method identifies frequency bands within the signal that likely correspond to the actual signal of interest.
  2. The offset is calculated based on the frequency range of the detected bands.
2. Frequency Shift Correction:
  1. Once the frequency offset is estimated, the signal is corrected by shifting its frequency. This is done by multiplying the signal with a complex exponential that counteracts the frequency offset.
  2. The correction is applied using the formula:
     y(t)=y(t)×exp⁡(j⋅2π⋅offset⋅t)
     where offset is the estimated frequency offset, and t is the time index.
3. Visual Confirmation:
  1. After the frequency shift correction, the signal is visualized, typically using a spectrogram, to verify that the frequency components align correctly with the expected range. This helps in confirming the effectiveness of the correction.

Step7: Frequency Spectrum Analysis After Offset Correction:
Compute FFT of the Corrected Packet:
- A Fast Fourier Transform (FFT) is applied to convert the time-domain signal into the frequency domain.
- The FFT output is shifted to center the zero frequency.
Plot Frequency Spectrum:
- The magnitude of the FFT is plotted against frequency to visualize the corrected signal's frequency components.
- This step helps confirm that the frequency shift correction has aligned the signal correctly in the spectrum.
Step8: Power Spectral Density (PSD) Analysis After Offset Correction:
Apply Hamming Window:
A Hamming window is applied to reduce spectral leakage before computing the PSD.
Compute PSD Using Welch’s Method:
The Welch method is applied to estimate the PSD of the corrected signal, using a defined FFT size.
Shift and Normalize PSD:
- The PSD and frequency values are shifted to center the zero frequency.
- The mean PSD value is calculated to assess the power distribution.
Plot the PSD:
- A log-scale plot of the PSD is generated to analyze the frequency components.
- The mean PSD level is highlighted to visualize signal strength relative to noise.
Step9: Apply a DFT-based low-pass filter to the signal packets after frequency offset correction:
After offset correction of the signal packets:
Filtering a signal using the DFT involves the following steps:
- Compute the DFT of the input signal packets using the np.fft.fft function.
- Multiply the DFT of the input signal packets with the frequency response of the desired filter.
- Compute the inverse DFT of the resulting product using the np.fft.ifft function to obtain the filtered signal.
Step10: Frequency Spectrum Analysis After Low-Pass Filtering:
FFT Analysis After Filtering:
- The filtered packets is transformed into the frequency domain using FFT.
- The frequency spectrum is analyzed to observe the impact of filtering.
- A plot of the FFT magnitude is generated to visualize the spectral content of the filtered signal.
Step11:PSD Calculation After Low pass Filtering:
PSD Calculation Using Welch's Method:
  - If the filtered packet is sufficiently long, a Hamming window is applied to minimize spectral leakage.
  - Welch’s method is then used to compute the Power Spectral Density (PSD) of the filtered signal. This method divides the signal into overlapping segments, performs the FFT on each segment, and averages the results to produce a smoother estimate of the PSD.
  - Both the frequency axis and the PSD values are shifted to include both positive and negative frequencies.
- Plotting and Analysis:
  - The PSD is plotted on a logarithmic scale to clearly show the power distribution across different frequencies.
  - The mean PSD value is calculated and displayed as a reference line on the plot to highlight the overall power levels in the signal.

Step12: Skewness and Kurtosis Calculation with KDE Plot for Filtered Signal Magnitude:
After filtering the corrected signal packets, we calculated the skewness and kurtosis using the following formulas:
- Skewness: Skewness = (n / ((n-1)(n-2))) * Σ ((x_i - μ) / σ)³
- Kurtosis: Kurtosis = (1 / n) * Σ ((x_i - μ) / σ)⁴ - 3
Where:
- nn is the number of samples in the signal,
- xix_i is each individual data point,
- μ\mu is the mean of the signal,
- σ\sigma is the standard deviation.
- Classification of Results:
  The skewness and kurtosis values were classified into categories:
  - Skewness:
    - Positive skewness indicates a longer tail to the right.
    - Negative skewness indicates a longer tail to the left.
    - Zero skewness indicates a symmetric distribution.
  - Kurtosis:
    - Leptokurtic (kurtosis > 3) indicates a sharp peak.
    - Platykurtic (kurtosis < 3) indicates a flat peak.
    - Mesokurtic (kurtosis = 3) indicates a normal distribution.
Then, we estimated the probability density function (PDF) of the magnitude of the filtered signal using Kernel Density Estimation (KDE). This method generates a smooth curve that represents the distribution of the signal, providing a clear visualization of its amplitude distribution.
### Step13: Method for Pattern Detection and Extraction Process:
Energy Calculation:
First, I computed the energy for each sample in the filtered signal by calculating the squared magnitude of each sample:
Energy=∣xi∣^2
- Energy Smoothing:
  Next, I applied a moving average to the energy curve using a specified window size to smooth the energy signal and reduce fluctuations.
- Pattern Detection:
  After that, I set an energy threshold to identify low-energy regions. If the smoothed energy falls below the threshold, I marked those regions as potential patterns. I then checked if these regions lasted for a specified duration (pattern_length) to confirm them as valid patterns.
- Pattern Extraction:
  Once the low-energy regions were detected, I extracted the corresponding signal segments as patterns based on the detected start and end indices.
- Visualization:
  Finally, I visualized the results by plotting the smoothed energy curve and highlighting the detected patterns. For each detected pattern, I calculated its energy, power, and number of samples, and then plotted both the time-domain signal and the spectrogram to analyze the pattern further.
Another way:

### 🛠️ Step-by-Step Working Procedure – Pattern Extraction from Filtered Signal Packets
### Step 1: Define Parameters
- Set the sampling rate
- Define the pattern duration .
- Compute the corresponding pattern length in samples .
#### Step 2: Select Reference Pattern
- Take the reference pattern from the first filtered packet starting at sample index .
- This pattern is used as a template for matched filtering.
#### Step 3: Iterate Through Filtered Packets
Loop through each filtered_packet in filtered_packets.
#### Step 4: Matched Filtering
- Compute cross-correlation between the filtered_packet and the reference pattern using magnitudes.
- Normalize the correlation output.
- Smooth the correlation using a moving average window to reduce noise.
#### Step 5: Adaptive Thresholding
- Compute the local mean and standard deviation of the smoothed correlation using a sliding window.
- Define an adaptive threshold:
  threshold = local_mean + k_factor * local_std
#### Step 6: Detect Pattern Locations
- Use scipy.signal.find_peaks() to detect peaks in the correlation output.
- Apply:
  - height ≥ adaptive threshold
  - prominence based on standard deviation
  - width to filter out narrow noise peaks
- Enforce a minimum gap between peaks to avoid overlapping patterns.
#### Step 7: Extract Detected Patterns
- For each detected peak index:
  - Extract a signal segment of samples (the pattern length).
- Store all patterns in all_extracted_patterns.
#### Step 8: Plotting
- Plot the smoothed correlation, adaptive threshold, and detected peaks.
- For each extracted pattern:
  - Plot its spectrogram to visualize frequency content over time.
#### Step 9: Pattern Statistics (Optional)
- (Optional block): Calculate and print:
  - Energy
  - Power
  - Mean amplitude
  - Amplitude variance of each pattern
#### Step 10: Final Summary
Print the total number of extracted patterns.

### Step14: Skewness and Kurtosis Computation for extracted pattern:
Moment-Based Skewness Calculation:
For each extracted pattern, the skewness was calculated using the magnitude of the signal. The formula for skewness is:
Skewness = (n / ((n - 1) * (n - 2))) * Σ((|x_i - μ|) / σ)^3
where:
- n = number of samples
- x_i = individual sample values
- μ = mean of the sample
- σ = standard deviation of the sample
- Moment-Based Kurtosis Calculation:
  Similarly, the kurtosis was calculated using the magnitude of the signal with the formula:
  Kurtosis:
  Kurtosis = (1 / n) * Σ((|x_i - μ|) / σ)^4 - 3
  This formula computes the excess kurtosis, where a value of 0 corresponds to a normal distribution.
- Classification of Results:
  The skewness and kurtosis values were classified into categories:
  - Skewness:
    - Positive skewness indicates a longer tail to the right.
    - Negative skewness indicates a longer tail to the left.
    - Zero skewness indicates a symmetric distribution.
  - Kurtosis:
    - Leptokurtic (kurtosis > 3) indicates a sharp peak.
    - Platykurtic (kurtosis < 3) indicates a flat peak.
    - Mesokurtic (kurtosis = 3) indicates a normal distribution.
### Visualization
For each pattern, a Kernel Density Estimation (KDE) plot was generated to estimate the probability density function (PDF) of the magnitude of the signal. This helps visualize the distribution of the signal amplitudes. The KDE provides a smooth curve that represents the shape of the distribution, making it easier to understand the statistical characteristics of the extracted patterns.